## Slide 1: Internet Of Things (IoT) Unit 2 –IoT Protocols
Raghu Prasad K S
Professor Of Practice
Kristu Jayanti College
9845547471

## Slide 2: Introduction
Raghu Prasad – BE, MS
Total of 29 years of experience
7 years as a lecturer in an Engineering College
22 Years into IT
Worked with companies like CISCO,CSC,ICICI,First Apex – NTT Data
Currently into Corporate training and consultancy
Worked with corporates and public sector
Service Offerings – In person/On-line/Corporate/Academic Institutes
Technologies – Java,Python,Web technologies,Java Script technologies (MEAN stack),IOT,Test Automation,Machine Learning,Artificial Intelligence,ERP,.NET
Customers – Philips,L & T,NextGen,Incarnus,BGS-IT,Sindhi College,Malnad Enginering College,S B College of Management, REVA University

## Slide 3: Topics
Introduction to IoT Protocols
Communication Technology
ISM Bands
Zigbee,Z-Wave,Bluetooth,BLE
MQTT
COAP
HTTP - REST

## Slide 4: IoT Protocols
What is a protocol ?
Special set of rules that end points in a telecommunication connection use when they communicate. Protocols specify interaction between the communicating entities.
Protocol | Technology | Standard
A network protocol defines rules and conventions for communication between network devices | Activity of designing and constructing and maintaining communication system | A standard is a document that specifies something that has the overwhelming support and agreement of the standards making body
Examples Protocols | Examples of Technology | Examples of standard
IP TCP UDP FTP HTTP MQTT COAP | Wi-Fi Bluetooth ZigBee NFC WiMax GSM CDMA | IEEE 802.11 a/b/g (WiFi,Bluetooth) 802.15 (ZigBee,NFC,GSM) 802.16

## Slide 5: IoT Protocols
IoT end node/device requirements
  Scalable
  Secure
  End node addressability
  Low power
  Limited memory
  Low cost
  Lightweight connection

## Slide 6: OSI Model(Open System Interconnect)

## Slide 7: Communication Technologies
ZigBee
Z-wave
Bluetooth
Bluetooth Low Energy (BLE)
Wi-Fi
Cellular
6LowPAN
LoRaWAN
Sigfox

## Slide 8: ISM bands

## Slide 9: Introduction to Zigbee in IoT
Zigbee is a low-power, low-data-rate wireless communication protocol commonly used in IoT applications. It is designed for efficient, secure communication in devices requiring minimal power consumption and operating over short ranges.

## Slide 10: Key Features of Zigbee in IoT
1. Low power consumption for battery-powered devices.
2. Mesh networking extends range and improves reliability.
3. Low data rate (20 kbps to 250 kbps) for small data transmissions.
4. Range of 10-100 meters, extendable through mesh.
5. Built-in 128-bit AES encryption for secure communication.
6. Cost-effective and scalable for large IoT deployments.

## Slide 11: Zigbee Architecture in IoT
Zigbee operates on top of the IEEE 802.15.4 standard and consists of:
- Physical Layer: Manages transmission and reception of data.
- MAC Layer: Controls access to the radio channel.
- Network Layer: Handles routing and addressing in the mesh network.
- Application Support Layer: Manages services and communication between devices.
- Application Layer: Defines protocols and profiles for specific applications.

## Slide 12: Use Cases of Zigbee in IoT
1. Smart Home: Lights, thermostats, and security systems.
2. Industrial Automation: Reliable communication in harsh environments.
3. Health Monitoring: Remote sensors for patient data.
4. Smart Metering: Real-time monitoring of energy usage.
5. Agriculture: Soil moisture and environmental monitoring.

## Slide 13: Comparison with Other IoT Protocols
1. Zigbee: Low power, mesh network, low data rate.
2. Wi-Fi: Higher power consumption, higher data rate.
3. Bluetooth Low Energy (BLE): Similar low power, shorter range.

## Slide 14: Zigbee-Summary
ZigBee
  Low data rate,Low power consumption,Small pocket devices,Unlicensed bands
Bands (ISM – The industrial, scientific, and medical radio band)
  ISM 2.4 GHz Global band at 250 kbps
  868 MHz European band at 20 kbps
  915 MHz North American band at 40 kbps
  Range is very low – 100 to 300 ft
  Topologies
  Mesh,Star,One to One
  Usage
  Building automation,Health care,Asset management,Consumer electronics,Lawn and garden irrigation

## Slide 15: Zigbee Network Topologies
Overview of different network topologies used in Zigbee

## Slide 16: ZigBee

## Slide 17: ZigBee – Network topology
  Mesh topology in detail

## Slide 18: ZigBee – Network

## Slide 19: Star Topology
• A central coordinator communicates with all other devices (end devices).
• Simple, but limited range as all devices must be within the coordinator's range.
• If the coordinator fails, the entire network fails.

## Slide 20: Tree Topology
• The network is hierarchical, with a coordinator at the root.
• Routers connect to the coordinator or other routers, forming branches.
• Extends range but relies on router communication; failure of routers can disconnect devices.

## Slide 21: Mesh Topology
Devices (routers and coordinator) can forward messages to extend the range.
High fault tolerance, messages can reroute if a device fails.
Highly scalable and suitable for large, reliable networks.

## Slide 22: Comparison of Topologies
Star: Simple but limited range, central coordinator.
Tree: Hierarchical with routers extending range.
Mesh: Highly scalable, fault-tolerant, and ideal for large networks.

## Slide 23: Z-Wave
Z-Wave
  Oriented towards residential control and automation market
Bands
  Works in sub Giga hertz frequency band – 900 MHz,100 kbps
  Can have a maximum of 232 nodes
  Topologies
  Operates on mesh network architecture with one primary and multiple secondary controllers
  USP is interoperability

## Slide 24: Introduction to Bluetooth and BLE
Bluetooth and Bluetooth Low Energy (BLE) are wireless communication technologies under the Bluetooth specification. While both are used in IoT, they differ significantly in power consumption, data rate, and use cases, making them suitable for different IoT applications.

## Slide 25: Bluetooth
Bluetooth
  Open standard for development of Personal Area Network (PAN)
  Low cost,low power, short range (with in 10 meters)
  Bluetooth enabled device can exchange information (transfer data) with other bluetooth device over a radio
  Bluetooth helps in creating small network of devices that are close to one another
  Bluetooth Low Energy (BLE)
    Integral part of Bluetooth specification from Bluetooth V4.0 onwards
    Low power consumption
    Wearables, home automation, Health and wellness, Sports and fitness

## Slide 26: BLE
Bluetooth Tooth Low Energy
  Integral part of Bluetooth core specification from v4.0 onwards
  Range : ~150 mtrs open field
  Output power: ~10 mW
  Max Current: ~15 mA
  Topology: Star
  Connection : >2 billlon
  Modulation : GFSK @2.4 GHz
  Security : 128 bit AES CCM

## Slide 27: BLE - Applications
BLE and Bluetooth Tooth applications

## Slide 28: Key Differences
1. Power Consumption: Bluetooth Classic is high-power, while BLE is designed for low power consumption.
2. Data Rate: Bluetooth Classic offers higher data rates (~2-3 Mbps), while BLE supports lower rates (~125 kbps to 1 Mbps).
3. Battery Life: BLE is optimized for devices with long battery life (months to years), whereas Bluetooth Classic has shorter battery life.
4. Use Cases: Bluetooth Classic is ideal for continuous connections (e.g., audio streaming), while BLE is better for periodic data transfer (e.g., sensors, trackers).

## Slide 29: Use Cases for IoT
Bluetooth Classic:
- Audio streaming (wireless speakers, headphones)
- File transfer and hands-free communication
Bluetooth Low Energy (BLE):
- Smartwatches, fitness trackers, medical devices
- IoT sensors, smart home devices, beacons
- Ideal for devices with low power needs and short, infrequent data transfers

## Slide 30: Summary of Bluetooth vs BLE for IoT
Bluetooth Classic is best for high-data, continuous applications, such as audio and file sharing, while BLE is optimized for energy-efficient, infrequent data transfers in IoT, such as fitness trackers and smart home sensors. For IoT, BLE is generally preferred due to its low power consumption and long battery life.

## Slide 31: Wi-Fi
Wi-Fi
  Widely used
  Standard – 802.11 n
  Frequencies – 2.4 to 5 GHz
  Range – 50 m
  Data rates – 600 Mbps max. Typically between 150 to 200 Mbps
  http://beta.speedtest.net

## Slide 32: Cellular
Cellular
  IOT application require to operate over longer distance can use GSM/3G/4G
  Standard – GSM/GPRS/Edge (2G)/UMTS/HSPA (3G)/LTE (4G)
  Frequencies – 900/1800/1900/2100 MHz
  Range – 35 kms max for GSM,200 Kms for HSPA
  Data rates (typical download)– 35 to 170 kbps (GPRS),120 to 384 kbps (EDGE),384 kbps to 2 Mbps (UMTS),600 kbps to 10 Mbps ( HSPA), 3 to 10 Mbs (LTE)

## Slide 33: 6LoWPAN
6LoWPAN
  IPv6 over low power Wireless Personal Area Network. Works with Mesh architecture
  A simple low cost wireless network of devices that have limited power and relaxed throughput requirements
  Has the capability to connect to internet
  Confirms to 802.15.4-2003
  It is an adaption layer for IPv6 over IEEE802.15.4 links

## Slide 34: 6LoWPAN

## Slide 35: 6LoWPAN
Nodes
(Self-healing mesh, routers and hosts)
From light bulbs to smoke detectors, each node carries an IPv6 address. Nodes typically require small amounts of memory and processing power, and can be implemented using a wireless microcontroller (MCU).
EDGE router
(Simple IP router, no-application-layer gateway)
The compressed IPv6 header needs an intermediary device to provide a conversion between 6LoWPAN and standard IP header. An EDGE router can be seen as this simplified “gateway”. This can be a standalone or an add-on system.
Internet
Connect to any cloud. TI is partnering with many cloud service providers to provide a simple and direct way to get you to the cloud.

## Slide 36: 6LoWPAN

## Slide 37: Sigfox
Sigfox
  Range comes between WiFi and Cellular
  Uses ISM bands which is free and no license is required
  Ideal for devices having low level of data transfer and communication should be less expensive
  Frequency – 900 MHz
  Range – 30 to 50 kms Rural, 3 to 10 kms Urban
  Data Range – 10 to 1000 bps

## Slide 38: LoRaWAN (Long Range Wide Area Network)
LoRaWAN targets wide-area network (WAN) applications and is designed to provide low-power WANs with features specially needed to support low-cost mobile secure bi-directional communication in IOT,M2M and smart city and industrial applications
Optimized for low-power consumption and supporting large networks with millions and millions of devices,data rates rages from 0.3 kbps to 50 kbps.
Standard:LoRaWAN
Frequency :Various
Range: 2-5 km (urban environment), 15 km(suburban environment)
Data Rates:0.-50 kpbs
https://www.techtarget.com/searchnetworking/answer/What-is-the-difference-between-LoRa-and-LoRaWAN

## Slide 39: Range vs Data rate

## Slide 40: IOT - Protocols

## Slide 41: Restful HTTP

## Slide 42: Restful HTTP

## Slide 43: Restful HTTP – Hands-on
https://jsonplaceholder.typicode.com/
Get method
https://jsonplaceholder.typicode.com/user
Get method with id
https://jsonplaceholder.typicode.com/user/1
https://openweathermap.org/api
http://api.openweathermap.org/data/2.5/weather?q=London&APPID=384db1ce93218e20fd384d3016372238

## Slide 44: MQTT (Message Queue Telemetry Transport)
MQTT stands for MQ Telemetry Transport. It is a publish/subscribe, extremely simple and lightweight messaging protocol, designed for constrained devices and low-bandwidth, high-latency or unreliable networks. The design principles are to minimise network bandwidth and device resource requirements whilst also attempting to ensure reliability and some degree of assurance of delivery. These principles also turn out to make the protocol ideal of the emerging “machine-to-machine” (M2M) or “Internet of Things” world of connected devices, and for mobile applications where bandwidth and battery power are at a premium.
http://mqtt.org/

## Slide 45: MQTT (Message Queue Telemetry Transport)
Lightweight message queuing and transport protocol
Low overhead (2 bytes header) for low network bandwidth applications
Publish/Subscribe (Pub Sub0 model
Simple protocol, aimed at low power and low footprint implementation (e,g. WSN-Wireless Sensor Networks)
Runs on connection-oriented transport(TCP)
Sensor and actor nodes communicate with applications through the MQTT message broker

## Slide 46: MQTT

## Slide 47: MQTT

## Slide 48: MQTT

## Slide 49: MQTT – Quality Of Service
Quality of Service (QoS) in MQTT messaging is an agreement between sender and receiver on the guarantee of delivering a message.
There are three levels of QoS: 0 - at most once. 1 - at least once. 2 - exactly once.
When a client (e.g. a remote IoT device) is publishing to a broker, the client determines the QoS level for that message. When the broker sends the message to a subscribing client, the QoS set by the first client for that message is used again.
So effectively the original publisher of any message determines the QoS of the message all the way to the final recipients.
https://assetwolf.com/learn/mqtt-qos-understanding-quality-of-service

## Slide 50: MQTT – Quality Of Service
http://www.steves-internet-guide.com/understanding-mqtt-qos-levels-part-1/

## Slide 51: MQTT - Features
Open
  Invented by IBM and Eurotech
  MQTT client code (C and Java) donated to the Eclipse “Paho” M2M project
  Reliable
    Three quality of Service
  Lean
  Minimized on-the-wire format
  Smallest possible packet size is 2 bytes
  No application message header
  Reduced complexity/footprint
  Clients:c=30 kb java=100kb
  Simple
  Simple/minimal pub/sub message semantic s
    Asynchronous (“push”) delivery
    Simple set of verbs – connect,publish,subscribe and disconnect

## Slide 52: MQTT – Case Study

## Slide 53: MQTT Brokers/Servers
Commercial
  IBM
  Software AG
  dcSQuare
  Open Source or free download
    Mosquitto (https://mosquitto.org/). Client – Chrome add-on – MQTTLens
    mosquitto_sub -h test.mosquitto.org -p 1883 -t “test”
    mosquitto_pub -h test.mosquitto.org -p 1883 -t “test” –m “this is for testing”
    RSMB
    ActiveMQ
    Apollo
    RabbitMQ
    Mqtt.js
    eMQTT

## Slide 54: MQTT Hands-on
    Download and install mosquitto mqtt broker
    https://mosquitto.org/download/
        Windows
        mosquitto-2.0.18a-install-windows-x64.exe (64-bit build, Windows Vista and up, built with Visual Studio Community 2019
    Verify whether mosquitto is running using windows search – services – mosquito
    Stop the mosquitto service
    Run mosquito from command prompt
    Cmd to C:\Program Files\mosquitto
        Type mosquito

## Slide 55: MQTT Hands-on
        6. Subscribe to a topic
        Open another terminal and cmd to C:\Program Files\mosquito
        Type mosquitto_sub -h localhost -p 1883 -t "topic”
        7. Publish a topic
        Open another terminal and cmd to C:\Program Files\mosquito
        Type mosquitto_pub -h localhost -p 1883 -t "topic" -m "Hello World“
        8. Check the subscriber whether you have received the message

## Slide 56: MQTT Hands-on
        Message for home automation
        Subscribe
        mosquitto_sub -h localhost -p 1883 -t "home/room1/sensor“
        3.Publish
        mosquitto_pub -h localhost -p 1883 -t "home/room1/sensor" -m "{\"roomtemp\":28.5, \"humidity\":65}“

## Slide 57: MQTT Hands-on – Python program
        Create mqttdemo folder
        cd to mqttdemo folder
        Create virtual environment using python –m venv venv
        Active virtual environment using .\venv\Scripts\activate
        Install paho-mqtt using
        pip install paho-mqtt
        6. Create mqttdemo_publish.py
        7. Create mqttdemo_subscribe.py
        8. Ensure that mosquitto broker is running
        8. Run both the programs using
        python mqttdemo_publish.py pip install paho-mqtt
        python mqttdemo_subscribe.py

## Slide 58: MQTT Hands-on – Python program
        mqtt_publish.py
        import paho.mqtt.client as mqtt
        import time
        # Define the callback functions
        def on_connect(client, userdata, flags, rc):
        if rc == 0:
        print("Connected successfully")
        #client.subscribe("test/topic")
        else:
        print(f"Connect failed with result code {rc}")
        def on_message(client, userdata, msg):
        print(f"Message received: {msg.topic} {msg.payload.decode()}")
        # Create an MQTT client instance
        client = mqtt.Client()
        # Assign the callback functions
        client.on_connect = on_connect
        client.on_message = on_message
        # Connect to the MQTT broker
        #client.connect("localhost", 1883, 60)
        client.connect("broker.hivemq.com", 1883, 60)

## Slide 59: MQTT Hands-on – Python program
        #continued from previous slide
        # Start the loop to process network traffic and dispatch callbacks
        client.loop_start()
        # Publish a message to the topic
        client.publish("test/topic", "message_payload")
        # Add a delay to give the client time to receive the message
        time.sleep(2)
        # Stop the loop and disconnect
        client.loop_stop()
        client.disconnect()

## Slide 60: MQTT Hands-on – Python program
        mqtt_subscribe.py
        import paho.mqtt.client as mqtt
        # Define the on_message callback
        def on_message(client, userdata, message):
        print(f"Received message '{message.payload.decode()}' on topic '{message.topic}' with QoS {message.qos}")
        # Create an MQTT client instance
        client = mqtt.Client()
        # Assign the on_message callback
        client.on_message = on_message
        # Connect to the MQTT broker
        client.connect("broker.hivemq.com", 1883, 60)
        #client.connect("localhost", 1883, 60)
        # Subscribe to a topic
        client.subscribe("test/topic")
        # Start the loop to process received messages
        client.loop_start()
        # Keep the script running
        import time
        while True:
        time.sleep(1)

## Slide 61: CoAP
Constrained Application Protocol – CoAP is a specialized web transfer protocol
Use with constrained nodes and constrained networks in IOT
The protocol is designed for machine-to-machine (M2M) applications such as
  Smart energy
  Building automation
  And may more

## Slide 62: CoAP overview
Inspired by HTTP (GET,POST,PUT, DELETE)
1-to-1 communication protocol
Lightweight and energy-efficient
Additional features on top of HTTP:
  Observe
  Discovery
QoS
  Confirmable messages
  Non-confirmable messages (fire and forget)

## Slide 63: CoAP feature

## Slide 64: CoAP

## Slide 65: CoAP

## Slide 66: MQTT vs CoAP

## Slide 67: Comparison of IOT protocol

## Slide 68: References
Edge Computing - https://www.youtube.com/watch?v=yRBe9YYCGw4
Right Protocol - https://www.youtube.com/watch?v=7eNU4rvdTC0&t=194s
Zigbee - https://www.youtube.com/watch?v=QXV_HgGO--g
NB-IOT - https://www.youtube.com/watch?v=F2YTUwh5-qE
ZigFox - https://www.youtube.com/watch?v=jcYoNvkorOY&t=5s
BLE - https://www.youtube.com/watch?v=NSkIHdV6NoY
OSI - https://www.youtube.com/watch?v=vv4y_uOneC0

## Slide 69: References
Zigbee-https://www.youtube.com/watch?v=2KcZcNkRrNU&ab_channel=MAKERDEMY
https://www.youtube.com/watch?v=QXV_HgGO--g&t=14s&ab_channel=MAKERDEMY
SOC -https://www.geeksforgeeks.org/architecture-of-soc/
OSI - https://www.linkedin.com/pulse/osi-model-explained-how-easily-remember-its-7-layers-rahul-jasrotia/

## Slide 70: References
Zigbee-
https://www.youtube.com/watch?v=QXV_HgGO--g&t=151s&ab_channel=MAKERDEMY
https://www.youtube.com/watch?v=Jmml-2Ge2WI&ab_channel=talkingStuffNetwork
https://www.youtube.com/watch?v=UmpDXc3cXbU&ab_channel=EverythingSmartHome
https://www.nic.in/blogs/lora-when-iots-talk-with-a-distance/
https://randomnerdtutorials.com/esp32-lora-rfm95-transceiver-arduino-ide/

## Slide 71: Thank You
Raghu Prasad K S
9845547471