## Slide 1: IEEE 802.15.4g Standard
Smart Utility Networks (SUN) – Extension of IEEE 802.15.4

## Slide 2: Introduction
• IEEE 802.15.4g is an amendment of IEEE 802.15.4 (2012).
• Defines PHY layer for Smart Utility Networks (SUNs).
• Designed for large-scale, outdoor, low-data-rate IoT systems.
• Focus: Smart Grid, Smart Meters, and Utility IoT.

## Slide 3: Frequency Bands
• 169 MHz (Europe)
• 450–470 MHz (U.S. utilities)
• 700–1000 MHz (sub-GHz ISM bands)
• 2.4 GHz ISM band (optional, less common)

## Slide 4: Modulation Schemes
• FSK (Frequency Shift Keying) → Robust, long-range
• OFDM (Orthogonal Frequency Division Multiplexing) → Higher data rates
• O-QPSK (Offset Quadrature Phase Shift Keying) → Similar to base IEEE 802.15.4

## Slide 5: Key Features
• Supports millions of nodes in large-scale networks
• Data rates: 10 kbps to 1 Mbps
• Long-range communication (kilometers with sub-GHz)
• Flexible PHY options for regional compliance
• Designed for multi-vendor interoperability

## Slide 6: Applications
• Smart Grid – Advanced Metering Infrastructure (AMI)
• Smart Meters – Gas, Water, Electricity
• Utility IoT – Distribution automation, demand-response
• City Infrastructure – Street lighting, smart parking

## Slide 7: Protocols Built on IEEE 802.15.4g
• Wi-SUN (Wireless Smart Utility Network)
• 6LoWPAN over 802.15.4g – IPv6 for Smart Meters
• Foundation for large-scale IoT utility deployments

## Slide 8: Summary
• IEEE 802.15.4g extends 802.15.4 for outdoor Smart Utility Networks.
• Operates in sub-GHz and ISM bands.
• Supports scalable, long-range, low-power IoT networks.
• Widely used in Smart Grid, Smart Meters, and Utility IoT.