## Slide 1: ISM Bands (Industrial, Scientific, and Medical Bands)
An overview of frequencies, uses, and real-world applications

## Slide 2: Introduction to ISM Bands
• ISM bands are radio frequency ranges reserved for Industrial, Scientific, and Medical purposes.
• Widely used for wireless communication due to unlicensed access.
• Shared by technologies like Wi-Fi, Bluetooth, RFID, and IoT.

## Slide 3: Common ISM Frequency Bands
• 6.78 MHz – Wireless power transfer
• 13.56 MHz – RFID, NFC, smart cards
• 27.12 MHz – Industrial heating, RFID
• 40.68 MHz – Industrial heating, short-range devices
• 433.05–434.79 MHz – Remote controls, IoT sensors
• 902–928 MHz – RFID, IoT (mainly in the U.S.)
• 2.400–2.4835 GHz – Wi-Fi, Bluetooth, Zigbee
• 5.725–5.875 GHz – Wi-Fi, wireless cameras
• 24.0–24.25 GHz – Radar, motion sensors

## Slide 4: Key Characteristics of ISM Bands
• Unlicensed use: Devices don’t need individual licenses but must follow regulations.
• Shared spectrum: Multiple users coexist, interference possible.
• Global adoption: 2.4 GHz band is the most popular worldwide.

## Slide 5: Real-World Applications of ISM Bands
• Microwave ovens → 2.45 GHz
• Wi-Fi routers → 2.4 GHz and 5 GHz
• Bluetooth headphones → 2.4 GHz
• RFID tags → 13.56 MHz / 915 MHz
• IoT sensors (LoRa, Zigbee) → 433 MHz / 868 MHz / 915 MHz