## Slide 1: Licensed vs Unlicensed Bands in India
Overview of spectrum allocation and purposes

## Slide 2: Licensed Bands: Cellular Mobile Services
• 700 MHz – 4G / 5G broadband
• 800 MHz – 2G/4G (CDMA/LTE)
• 900 MHz – 2G GSM, LTE
• 1800 MHz – 2G/4G LTE
• 2100 MHz – 3G / 4G / 5G
• 2300 MHz – 4G LTE (BWA)
• 2500 MHz – 4G LTE
• 3300–3600 MHz – 5G services
• 26 GHz (mmWave) – 5G high speed

## Slide 3: Licensed Bands: Broadcasting Services
• 470–698 MHz – Terrestrial TV (Doordarshan)
• 88–108 MHz – FM Radio
• 526.5–1606.5 kHz – AM Radio
• 3–30 MHz – Shortwave radio (AIR)

## Slide 4: Licensed Bands: Satellite Communication
• C-Band (3.4–4.2 GHz DL / 5.85–6.425 GHz UL) – Satellite TV, VSAT
• Ku-Band (10.7–12.75 GHz DL / 14–14.5 GHz UL) – DTH, VSAT
• Ka-Band (27–31 GHz) – High-throughput satellites (HTS)

## Slide 5: Licensed Bands: Defence & Public Safety
• Defence: HF, VHF, UHF, S-band, X-band
• Public Safety: 150–174 MHz (Police, Fire, EMS)
• 380–400 MHz (Railways, disaster management)
• 865–867 MHz (RFID / Smart metering, partly licensed)

## Slide 6: Unlicensed (Delicensed) Bands in India
• 2.4 GHz (2400–2483.5 MHz) – Wi-Fi, Bluetooth, IoT
• 5.8 GHz (5725–5875 MHz) – Wi-Fi, wireless cameras
• 865–867 MHz – RFID, IoT (low power use)
• 433 MHz (433.05–434.79 MHz) – IoT devices, short-range communication

## Slide 7: Comparison: Licensed vs Unlicensed Bands
Band Type | Examples | Purpose
Licensed Bands | 700 MHz, 900 MHz, 1800 MHz, 3300 MHz, 26 GHz | Mobile services (2G/3G/4G/5G), TV, Radio, Satellite
Govt/Defence Licensed | HF, VHF, UHF, X-band | Military, Railways, Emergency services
Unlicensed Bands | 2.4 GHz, 5.8 GHz, 433 MHz, 865–867 MHz | Wi-Fi, Bluetooth, RFID, IoT
Regulation | Auctioned by DoT/WPC | Delicensed for public use (with power limits)